## Slide 2
Shade Rule Redesign
Hawk Stone FPAC January 31 2020
Gary Hess

## Slide 3: Perspectives
SHADE STUDY
“The rule is effective”
“The rule is protective”
“The rule keeps shade loss <10%”
FIELD PRACTICE
“The rule is cumbersome”
“The rule is confusing”
“The rule is imprecise”
PUBLIC COMMENT
“The rule is difficult”
“The rule is complicated”
“The rule is hard to understand”

## Slide 4: WHAT IF…?
Adjacent to all Class I streams, to maintain and enhance shade and large woody debris recruitment, landowners must comply with one of the two following options defining tree retention. The Relative Stocking per acre (RS) referenced in the options is calculated according to the relative-stocking-contribution table in Subsection 030.07.e.ii. (3-20-14)
(1) Option 1: Within twenty-five (25) feet from the ordinary high water mark on each side of the stream, live conifers and hardwoods will be retained to maintain a minimum relative stocking per acre of sixty (60). A relative stocking per acre of thirty (30) must be retained in the stream protection zone between twenty-five (25) feet and seventy-five (75) feet from the ordinary high water mark on both sides of the stream. (3-20-14)
(2) Option 2: Within fifty (50) feet from the ordinary high water mark on each side of a stream, live conifers and hardwoods will be retained to maintain a minimum relative stocking per acre of sixty (60). A relative stocking per acre of ten (10) must be retained in the stream protection zone between fifty (50) feet and seventy-five (75) feet from the ordinary high water mark on both sides of the stream. (3-20-14)
(3) Only one (1) option may be implemented within the stream protection zones of a harvesting unit covered by a single notification. Landowners are strongly encouraged to retain all trees immediately adjacent to the stream.
Forest Type Per Tree Contribution to Relative Stocking by Diameter Class
Diameter Class (DBH in inches)
4-7.9" 8-11.9" 12-15.9" 16-19.9" 20-23.9" 24-27.9" 28-31.9"
NIGF (North Idaho Grand Fir) 0.097 0.209 0.347 0.506 0.683 0.878 1.088
CIGF (Central Idaho Grand Fir) 0.113 0.244 0.405 0.59 0.797 1.024 1.27
SIGF (Southern Idaho Grand Fir) 0.136 0.293 0.486 0.708 0.957 1.229 1.524
WHSF (Western Hemlock-Subalpine Fir)0.123 0.267 0.442 0.644 0.87 1.117 1.385
DFPP (Douglas-fir-Ponderosa Pine) 0.151 0.326 0.54 0.787 1.063 1.366 1.693
24. Forest Type. Five forest types in Idaho are defined as follows: (3-20-14)
a. North Idaho grand fir/western red cedar (NIGF): moist to wet interior forests with western red cedar, western hemlock, and grand fir being primary climax species, found in forests north of the Clearwater/ and Lochsa Rivers. (3-20-14)
b. Central Idaho grand fir/western red cedar (CIGF): productive conifer forests found in forests between the Lochsa River Basin and the Salmon River, characterized by stands having western red cedar and grand fir as climax species, with a mixed-conifer overstory increasingly comprised of ponderosa pine, Douglas-fir, and larch in the river breaks canyon-lands. Stocking levels are generally lower than that of the NIGF stands. (3-20-14)
c. South Idaho grand fir (SIGF): mixed-conifer forests, dominated by ponderosa pine and Douglas-fir, found south of the Salmon River with grand fir and occasionally western red cedar being the stand climax species. (3-20-14)
d. Western hemlock-subalpine fir (WH): higher-elevation, moist, cool interior forests dominated by western hemlock, mountain hemlock, and/or subalpine fir. (3-20-14)
e. Douglas-fir-ponderosa pine (PP): drier forests dominated by ponderosa pine and Douglas-fir, generally found in lower-elevation, dry sites. (3-20-14)

## Slide 6: Step 1 – Use Only 60/30 Option
Benefits:
  Simplicity
  Resource protection
  Closer to the science
  Doesn’t limit harvest
  Encourages deeper SPZ management
  Avoids one particular problematic harvest type
60 30 30
60 60 10
35

## Slide 7: Step 2 – Convert to Tree Count
 | 4 - 7.9” | 8 - 11.9” | 12 -15.9” | 16 -19.9” | 20 -23.9” | 24 -27.9” | > 28”
NIGF |  |  |  |  |  |  | 
CIGF |  |  |  |  |  |  | 
SIGF |  |  |  |  |  |  | 
WHSF |  |  |  |  |  |  | 
DFPP |  |  |  |  |  |  | 
 | 0.113 | 0.244 | 0.405 | 0.590 | 0.797 | 1.024 | 1.270
 | 0.136 | 0.293 | 0.486 | 0.708 | 0.957 | 1.229 | 1.524
 | 0.123 | 0.267 | 0.442 | 0.644 | 0.870 | 1.117 | 1.385
 | 0.151 | 0.326 | 0.540 | 0.787 | 1.063 | 1.366 | 1.693
 |  | 0.209 | 0.347 | 0.506 | 0.683 | 0.878 | 1.088
 |  | 287 | 173 | 119 | 88 | 68 | 55
 | 0.097 |  |  |  |  |  | 
 | 619 |  |  |  |  |  | 
 | 531 | 246 | 148 | 102 | 75 | 59 | 47
 | 441 | 205 | 123 | 85 | 63 | 49 | 39
 | 488 | 225 | 136 | 93 | 69 | 54 | 43
 | 397 | 184 | 111 | 76 | 56 | 44 | 35
Idea: Work backwards – set an RS target (60) and convert to trees per acre:
Current Rule
Tree count per acre for RS of 60 |  |  |  |  |  |  | 
Per-tree contribution to RS (per acre) |  |  |  |  |  |  | 

## Slide 8
 | 4 - 7.9” | 8 - 11.9” | 12 -15.9” | 16 -19.9” | 20 -23.9” | 24 -27.9” | > 28”
NIGF |  |  |  |  |  |  | 
CIGF |  |  |  |  |  |  | 
SIGF |  |  |  |  |  |  | 
WHSF |  |  |  |  |  |  | 
DFPP |  |  |  |  |  |  | 
 |  | 287 | 173 | 119 | 88 | 68 | 55
 | 619 |  |  |  |  |  | 
 | 531 | 246 | 148 | 102 | 75 | 59 | 47
 | 441 | 205 | 123 | 85 | 63 | 49 | 39
 | 488 | 225 | 136 | 93 | 69 | 54 | 43
 | 397 | 184 | 111 | 76 | 56 | 44 | 35
Tree count per acre for RS of 60 |  |  |  |  |  |  | 
Step 3 – Take out Tree Diameters
Relative Weighting |  |  |  |  |  |  | 
 | 1.00 | 2.16 | 3.58 | 5.22 | 7.04 | 9.05 | 11.22
Relative weighting | 1.00 | 2.16 | 3.58 | 5.22 | 7.05 | 9.06 | 11.24
Relative weighting | 1.00 | 2.15 | 3.57 | 5.21 | 7.04 | 9.04 | 11.21
Relative weighting | 1.00 | 2.17 | 3.59 | 5.24 | 7.07 | 9.08 | 11.26
Relative weighting | 1.00 | 2.16 | 3.58 | 5.21 | 7.04 | 9.05 | 11.21
619 in NIGF, 531 in CIGF, 441 in SIGF, 488 in WHSF, 397 in DFPP.
Weighted tree count per acre:
AVERAGE WEIGHTING | 1.00 | 2.16 | 3.58 | 5.22 | 7.05 | 9.06 | 11.23

## Slide 9: Step 4 – Convert to Linear Tree Count
So far, “trees per acre”
But “trees per 100 feet” is easier and more intuitive
Area of inner zone = 25’ x 100’ = 2500sf = 0.0574 acres
Before:
Weighted tree count per acre: 619 in NIGF, 531 in CIGF, 441 in SIGF, 488 in WHSF, 397 in DFPP.
Now:
Weighted tree count per one hundred feet of class I stream:
35.5 in NIGF, 30.5 in CIGF, 25.3 in SIGF, 28.0 in WHSF, 22.8 in DFPP.

## Slide 10: Step 5 – Extend to Outer Zone
Bonus from using only 60/30 option:
  RS 60 has exactly TWICE the tree density of RS30
  But the inner zone is exactly HALF the area of the outer zone
  These cancel out, so the linear tree count is identical for both zones

## Slide 11: Combine Steps 1-5
Within twenty-five feet and between twenty-five and seventy-five feet of the ordinary high water mark, leave the following weighted tree count per one hundred feet of class I stream, dependent upon forest type: 35.5 in NIGF, 30.5 in CIGF, 25.3 in SIGF, 28.0 in WHSF, 22.8 in DFPP.
We Could Stop Here
  Mathematically identical
  Intuitive
  Simpler
Calculate weighted tree count by multiplying the number of live trees of each diameter class by the weighting factor below, and then sum the results:

## Slide 13: Step 6: Simplify Forest Types
Chart: 
| NIGF | CIGF | WHSF | SIGF | DFPP
 | 35.5 | 30.5 | 28 | 25.3 | 22.8
Northern Region
Southern Region
…weighted tree count, dependent upon forest type:
35.5 in NIGF, 30.5 in CIGF, 25.3 in SIGF, 28.0 in WHSF, 22.8 in DFPP
Occurs throughout state
Notes: Idea – convert into two types, that align with the existing forest regions. Can’t work because it allows too much extra harvest in NIGF and restricts harvest in DFPP.

## Slide 14: Step 6 - Simplify Forest Types
WAS:
...retain the following weighted tree count per one hundred feet of stream, dependent upon forest type:
35.5 in NIGF,
30.5 in CIGF,
25.3 in SIGF,
28.0 in WHSF,
22.8 in DFPP.
NOW:
… retain the following weighted tree count per one hundred feet of stream:
35.5 north of the Clearwater/Lochsa Rivers,
30.5 between the Salmon and Clearwater/Lochsa Rivers,
25.3 south of the Salmon River,
22.8 in any stream dominated by Douglas fir and ponderosa pine.

## Slide 15: Step 7 - Condense Size Classes
…leave the following weighted tree count per one hundred feet of stream:
35.5 north of the Clearwater/Lochsa Rivers
30.5 between the Salmon and Clearwater/Lochsa Rivers
25.3 south of the Salmon River
22.8 in any stream protection zone dominated by Douglas fir and ponderosa pine.
1.58 4.40 8.05 11.23
1.37 3.83 7.00 9.76
Causes 15 % harvest increase; Reduce weighting by 15%
1.00 2.79 5.10 7.10
1
3
5
7
16.6
18.4
22.2
25.8
17
18
22
26
Normalize by dividing size classes and tree counts by 1.37

## Slide 16: Final Step – Combine
Within twenty-five feet and between twenty-five and seventy-five feet of the ordinary high water mark, leave the following weighted tree count per one hundred feet of class I stream: 26 north of Clearwater/Lochsa Rivers, 22 between Clearwater/Lochsa and Salmon Rivers, 18 south of Salmon River, and 17 in any stream protection zone dominated by Douglas fir and ponderosa pine.
Calculate weighted tree count by multiplying the number of live trees present in each diameter class by the weighting factor below and then sum the results:
Diameter Class (inches) | 4–11.9 | 12–19.9 | 20–27.9 | >28
Weight | 1 | 3 | 5 | 7

## Slide 17: Summary of Steps
Use only one harvest option (60/30)
Convert to “tree count”
Unpackage tree diameters from table
Reformulate to linear tree count
Extend to outer zone (same tree count)
Simplify forest types into geographic regions
Condense 7 diameter classes to 4
RESULT: Simple formulation, supported by the same science as the original rule.

## Slide 18: Questions?
Adjacent to all Class I streams, to maintain and enhance shade and large woody debris recruitment, landowners must comply with one of the two following options defining tree retention. The Relative Stocking per acre (RS) referenced in the options is calculated according to the relative-stocking-contribution table in Subsection 030.07.e.ii. (3-20-14)
(1) Option 1: Within twenty-five (25) feet from the ordinary high water mark on each side of the stream, live conifers and hardwoods will be retained to maintain a minimum relative stocking per acre of sixty (60). A relative stocking per acre of thirty (30) must be retained in the stream protection zone between twenty-five (25) feet and seventy-five (75) feet from the ordinary high water mark on both sides of the stream. (3-20-14)
(2) Option 2: Within fifty (50) feet from the ordinary high water mark on each side of a stream, live conifers and hardwoods will be retained to maintain a minimum relative stocking per acre of sixty (60). A relative stocking per acre of ten (10) must be retained in the stream protection zone between fifty (50) feet and seventy-five (75) feet from the ordinary high water mark on both sides of the stream. (3-20-14)
(3) Only one (1) option may be implemented within the stream protection zones of a harvesting unit covered by a single notification. Landowners are strongly encouraged to retain all trees immediately adjacent to the stream.
Forest Type Per Tree Contribution to Relative Stocking by Diameter Class
Diameter Class (DBH in inches)
4-7.9" 8-11.9" 12-15.9" 16-19.9" 20-23.9" 24-27.9" 28-31.9"
NIGF (North Idaho Grand Fir) 0.097 0.209 0.347 0.506 0.683 0.878 1.088
CIGF (Central Idaho Grand Fir) 0.113 0.244 0.405 0.59 0.797 1.024 1.27
SIGF (Southern Idaho Grand Fir) 0.136 0.293 0.486 0.708 0.957 1.229 1.524
WHSF (Western Hemlock-Subalpine Fir)0.123 0.267 0.442 0.644 0.87 1.117 1.385
DFPP (Douglas-fir-Ponderosa Pine) 0.151 0.326 0.54 0.787 1.063 1.366 1.693
24. Forest Type. Five forest types in Idaho are defined as follows: (3-20-14)
a. North Idaho grand fir/western red cedar (NIGF): moist to wet interior forests with western red cedar, western hemlock, and grand fir being primary climax species, found in forests north of the Clearwater/ and Lochsa Rivers. (3-20-14)
b. Central Idaho grand fir/western red cedar (CIGF): productive conifer forests found in forests between the Lochsa River Basin and the Salmon River, characterized by stands having western red cedar and grand fir as climax species, with a mixed-conifer overstory increasingly comprised of ponderosa pine, Douglas-fir, and larch in the river breaks canyon-lands. Stocking levels are generally lower than that of the NIGF stands. (3-20-14)
c. South Idaho grand fir (SIGF): mixed-conifer forests, dominated by ponderosa pine and Douglas-fir, found south of the Salmon River with grand fir and occasionally western red cedar being the stand climax species. (3-20-14)
d. Western hemlock-subalpine fir (WH): higher-elevation, moist, cool interior forests dominated by western hemlock, mountain hemlock, and/or subalpine fir. (3-20-14)
e. Douglas-fir-ponderosa pine (PP): drier forests dominated by ponderosa pine and Douglas-fir, generally found in lower-elevation, dry sites. (3-20-14)

## Slide 19: Questions?
Within twenty-five feet and between twenty-five and seventy-five feet of the ordinary high water mark, leave the following weighted tree count per one hundred feet of class I stream: 26 north of Clearwater/Lochsa Rivers, 22 between Clearwater/Lochsa and Salmon Rivers, 18 south of Salmon River, and 17 in any stream protection zone dominated by Douglas fir and ponderosa pine.
Calculate weighted tree count by multiplying the number of live trees present in each diameter class by the weighting factor below and then sum the results: